## Slide 1: Accelerated Bridge Construction in High Seismic Zones
M. Saiid Saiidi
Professor, Civil & Environmental Engineering
University of Nevada, Reno

## Slide 2: Why high seismic zone matters?
ABC relies on precast members that are connected in the field.

## Slide 3: Seismic Performance Requirement for Bridges (cast-in-place or precast)
No collapse under strong earthquakes
Plastic hinging of columns- structural fuse
Capacity-protected cap beams and footings
ABC connections must ensure
  Column plastic hinging
  No damage to cap beams and footings

## Slide 4: Post-Earthquake Column Damage State
Conventional
Plastic hinging of columns- structural fuse
ABC
Plastic hinging of columns- structural fuse
QUESTION: Does ABC provide opportunity to raise the standard?
Severe Damage

## Slide 5: Connecting Columns to Cap Beams/Footings
Coupler Option
Grouted sleeves
Headed bar couplers
Swaged
Shear screw
Non-Coupler Option
Grouted ducts
Prestressed systems
Pocket connections
Embedded columns
Others
Pins/hinges
Replaceable connections
Etc.

## Slide 6: Coupler (Mechanical Bar Splice) Connections
Common in non-seismic applications
Code | Coupler Type | Plastic Hinge
AASHTO | Full Mech. Connection | No
Caltrans | Service | No
 | Ultimate | No
ACI | Type 1 | No
 | Type 2 | Yes

## Slide 7: Recent Seismic Studies of Columns w/ Couplers
Grouted Couplers in Nevada, Utah, Florida
Displacement ductility of 4.5 or more
Headed Bar Couplers in Nevada
Displacement ductility of 7- same as CIP
QUESTION: Should the ban on couplers in plastic hinges be removed?

## Slide 8
Grouted
ducts
Prestressed Systems
Non-Coupler Option
Grouted ducts
Prestressed systems
Pocket connections
Embedded columns

## Slide 9
Ring
anchorage
Concrete-filled tube
column
Pocket Connections
Embedded
Columns

## Slide 10: Recent Seismic Studies of Non-Coupler Connections Show Excellent Performance
QUESTION: Which one to use?
Anecdotal evidence: The one that is closest to conventional design– Grouted ducts?
Anchor column bars properly; no other design considerations

## Slide 11
Others
Pins/hinges
Replaceable connections
Etc.
Hinges are common in California and Nevada bridge columns

## Slide 12: ABC Terminology- “Emulative”